## Slide 1: The coming era of Heterogeneous System Architecture(HSA)
BOFIN BABU – 2013H313085H

## Slide 2: What are Heterogeneous Systems?
Current CPUs and GPUs are designed as separate processing elements and do not work together efficiently.
Each has a separate memory space, requiring an application to explicitly copy data from CPU to GPU and then back again.
Heterogeneous Systems are improved system designs that enable CPU and GPU work together seamlessly.

## Slide 3: A comparison of CPU and GPU cores
 | CPU | GPU
Core | OOO Superscalar | IO SIMD
Branch Predictor | Available | N/A
TLP | 1 to 4 way Simultaneous Multithreading | abundant
Memory | Latency-limited | Bandwidth-limited
Latency Tolerance | Caching | Caching, Multithreading

## Slide 4: HSA: Some things to consider..
1. H/W arrangement
Possible placements for a ring network
2. Arbitration Policy
  Dispute b/w CPU and GPU
  Give higher priorities to CPU applications as they are more latency sensitive
  Make sure that when CPU and GPU applications are both bandwidth sensitive, CPU gets it’s fair share

## Slide 5: ..HSA: Some things to consider
3. Routing Algorithm
Needs better routing algorithms since normal algorithms may result in link congestion in the HSA.
Shortest distance algorithm: GPU packets prefer lower link while CPU packets prefer upper link. Fig: Intel’s Sandy Bridge
4. Resource Contention and Partitioning
  CPU and GPU packets compete for resources.
  Usually higher demanding cores (GPUs) acquire the most resources.
  Need portioning mechanisms

## Slide 6: A case study
Performance of Haar Face Detect (a commonly used multi-stage video analysis algorithm)
HW Configuration
4GB RAM; Windows 7 (64-bit); OpenCL 1.1
APU: AMD A10 4600M with Radeon™ HD Graphics
CPU: 4 cores @ 2.3 MHz (turbo 3.2 GHz)
GPU: AMD Radeon HD 7660G, 6 compute units, 685MHz
RESULTS
  2.3X performance gain
  2.4X reduced power level
Courtesy : AMD

## Slide 7: OpenCL and HSA
OpenCL framework for writing programs that execute across heterogeneous platforms
OpenCL can be used to give an application access to a graphics processing unit for non-graphical computing
HAS is an optimized platform architecture for OpenCL
Accelerating JAVA
Convert JAVA Bytecode to OpenCL using Aparapi

## Slide 8: Reference
Lee, Li, Kim: Design Space Exploration of On-chip Ring Interconnection for a CPU-GPU Architecture
HSA Foundation (http://www.hsafoundation.com)
AMD’s developers guide to Heterogeneous Computing (http://developer.amd.com/resources/heterogeneous-computing)
Diagrams in this presentation are taken from (1) and (2)